## Slide 1: Path Planning
Presentation 12/29/2021

## Slide 2: Today we'll focus on the path planning part
Earlier we've seen how to create a Map and Locoalization for SLAM purposes

## Slide 3: When node receives goal pose, it links to components (global, planner, local planner, costmaps and recovery behaviors) and outputs a velocity command
move_base node: moves robot from its current position to goal position
It sends geometry_msgs/Twist to /cmd_vel Topic
The move_base pkg
It takes a goal pose w/ msg type: geometry_msgs/PoseStamped

## Slide 4
Navigation Stack Setup

## Slide 5: DEF: Map representing cost of traversing different areas
Costmaps
Represents either a free space or places where robot would be in collision {0,255}
2 types: global costmap (static map) & local costmap (sensor's readings)
Costmap params defined in 3 files:
1) global_costmap_params.yaml
2) local_costmap_params.yaml
3) common_costmap_params.yaml

## Slide 6: 2 types: global planner & local planner
Planners
gp in charge of calculating safe path to arrive at goal pose (static map)
Note: gp won't calculate dynamic obstacles (bc not in static map)
Gp: NavfnROS, Carrot Planner, GlobalPlanner
Lp: DWA (Dynamic Window Approach)
Each planner has its own params, which modify the way planner behaves

## Slide 7: 1) RViz: 2D Nav Goal Tool 2) rostopic pub /move_base/goal move_base_msgs/MoveBaseActionGoal {} 3) Create Action Server : Use actionlib pkg to create servers executing long-running goals Need to define goal, result, feedback msgs (in action dir --> .action file) See send_goal_client.py file Here, action server: move_base
Send a goal pose

## Slide 8
Next: Path Planning part 2: Obstacle Avoidance