BLAM

BLAM is in structure quite similar to LOAM, with a scan matcher determining odometry running concurrently with a scan matcher adding scans to the map. No real documentation of the method is available other than instructions in the git repository. Thus, the following description is based very much on code. The algorithm is mainly chosen for testing due to its inclusion of loop closure mechanisms.

The BLAM SLAM solution can be viewed as a series of sub tasks performed each time a new point cloud is received from the LIDAR sensor or the bag. First, a series of filters are applied , including downsampling through a random downsampling filter and a voxel grid filter, and removal of outliers through identifying statistical outliers and points without a sufficient number of neighbors with a given radius. Once filtered, odometry is estimated using ICP. The estimated rigid transformation is then transformed to the world frame, which is then used to transform the filtered point cloud. Wit this point as basis, a nearest neighbour search in the existing map is performed as well.

Further those nearest neighbours are transformed back to the sensor frame, and localization in the map is found again using ICP. Before updating the map, the pose is checked for loop closures. For this, LAM uses GTSAM as a back-end. The transformed point cloud is attempted matched with point clouds from nearby poses using ICP. A pose graph is maintained along with current loop-closure radius. If a loop closure is found, the map is regenerated before inserting new points to the map.

Contrary to LOAM, BLAM computes loop closures. This is done using GTSAM as a back-end, ICP scan matching with nearby poses.